## Slide 1: Motion-Triggered Security Camera
Using OpenCV: frame differencing and contour tracking
CSC 126 · Computer Vision · Midterm Project
[Name 1] · [Name 2] · [Name 3]
MOTION DETECTED
Moving Objects: 1
Notes: Member 1 · 0:00-0:45. Greet the class, introduce the team and the project title. Script: Presentation_Script.md, Slide 1.

## Slide 2: The Problem
Expensive
Commercial security systems cost too much for small homes and shops
Tiring
Watching camera footage all day is exhausting and unreliable
Wasteful
24/7 recording fills storage, and most footage has no activity
Our solution: a low-cost webcam system that stays idle and reacts only when something moves.
Notes: Member 1 · 0:45-2:00. Expensive systems, tiring to watch, wasteful storage. Then introduce the solution.

## Slide 3: Objectives
1
Prepare frames with image operations
2
Separate moving regions from the background (segmentation)
3
Detect, track, and count moving objects
4
Show status, object count, date and time on screen
5
Auto-save timestamped screenshots when motion occurs
Notes: Member 1 · 2:00-3:00. Read the four main objectives, then pass to Member 2.

## Slide 4: Techniques Used
a
Image Operations
resize · cvtColor · GaussianBlur
Standardize frames, convert to grayscale, remove camera noise
b
Image Segmentation
absdiff · threshold · dilate
Build a binary motion mask from frame differences
e
Motion and Object Tracking
findContours · contourArea · boundingRect
Detect, filter, and box the moving objects
Notes: Member 2 · 3:00-5:00. Explain each topic: a. image operations, b. segmentation, e. motion tracking.

## Slide 5: Processing Pipeline
1
Capture a video frame
2
Resize, grayscale, Gaussian blur
3
absdiff with the previous frame
4
Threshold (25) and dilate
5
Find contours, keep area > 3000
6
Draw boxes, status, count, time
7
Save screenshot (5 s cooldown)
8
Show frame and motion mask
a. Image Operations
b. Segmentation
e. Motion Tracking
Output
The current frame becomes the previous frame in the next loop.
Notes: Member 2 · 5:00-6:00. Walk through the 8 steps left to right. Stress the last line: current frame becomes previous frame.

## Slide 6: How Frame Differencing Works
1. Camera frame
2. Motion mask
Static areas become black. Moving areas become white.
Notes: Member 2 · 6:00-6:45. Left: camera frame with the detected phone. Right: the motion mask. absdiff + threshold + dilate turn changed pixels white and static pixels black.

## Slide 7: Settings and Testing Results
Program settings (default)
Frame size | 800 × 600
Blur kernel | 21 × 21
Threshold | 25
MIN_CONTOUR_AREA | 3000 px
CAPTURE_COOLDOWN | 5 sec
Chart: Detection rate (% of 272 frames)
| A: Sensitive | B: Original | C: Less sensitive
Detection rate (%) | 84.93 | 68.75 | 43.01
Min area / threshold / dilation: A 500 / 20 / 2 · B 3000 / 25 / 2 · C 5000 / 30 / 3
Test B kept as default: cleaner boxes (about 2 per frame vs 9 for Test A). Test A is best when small movement matters.
Notes: Member 2 · 6:45-8:15. All 3 tests used the same 272-frame video. Detection rate = sensitivity, not accuracy. Test C missed small movement. All three detected large and slow movement.

## Slide 8: Live Demo
MONITORING
MOTION DETECTED
python main.py
Press Q to quit
Backup: samples/demo.mp4
1
Stay still: MONITORING, count 0
2
Wave a hand: MOTION DETECTED + box
3
Two moving objects: count goes up
4
Stop moving: back to MONITORING
5
captures/ folder: saved screenshots
Notes: Member 3 · 8:15-11:45. Run python main.py with the Motion Mask window beside the main window. If the webcam fails, set CAMERA_INDEX to samples/demo.mp4.

## Slide 9: Results
Monitoring
Green status, count 0, nothing is moving
Motion detected
Red status, bounding boxes, count, date and time
Saved capture
Timestamped screenshot saved in captures/
Notes: Member 1 · 11:45-12:15. Output is clear: status, boxes, count, date and time, and the saved screenshot includes all overlays.

## Slide 10: Limitations
Lighting and shadows
Sudden brightness changes and moving shadows can trigger false motion
Slow or stopped objects
Only consecutive frames are compared, so stopped objects disappear
Merged or split boxes
Nearby objects can merge into one box, so the count is approximate
No identification
It sees movement, but cannot tell a person from an animal
Camera movement
If the camera shakes, the whole frame looks like motion
Limited testing
All tests used one video; more scenes and lighting are needed
Notes: Member 1 · 12:15-13:30. Be honest about limitations. Test C missed small movement; only one video was tested.

## Slide 11: Possible Improvements
Background subtraction
MOG2 handles lighting changes and slow movement better
Region of interest
Only important areas trigger alerts
Alerts
Sound, email, or SMS notifications
Video clips
Record short clips, not only images
Person check
Use a Haar cascade to confirm a person is present
More testing
More videos, lighting conditions, and movement speeds
Notes: Member 2 · 13:30-14:15. Mention MOG2 background subtraction first, then the rest.

## Slide 12: Conclusion
Preprocessing strongly affects detection quality
Parameter tuning balances sensitivity and false alarms
Classical OpenCV can solve a real problem without machine learning
Thank you!
Questions?
github.com/bevvy-boop/motion-security-camera
Code · README · samples · screenshots · testing
Notes: Member 3 · 14:15-15:00. State the key learnings, show the GitHub link, then open for Q&A.